## Slide 1
Cyber-Physical Molding Station with Integrated IoT Monitoring and Secure Access

## Slide 2
CONTENTS
1. Introduction
3. Node Architecture
5. Key Features
7. Applications
2. System Overview
4. Functional Workflow
6. Hardware & Software
8. Future Enhancements

## Slide 3
01
Introduction

## Slide 4
Introduction
This project implements Cyber-Physical System (CPS) for a smart molding station. The system integrates 8 nodes for real-time monitoring, control, and security of environmental parameters, machine health, and automated material handling. A 3D digital twin visualizes the live data and enforces bidirectional feedback, ensuring that access permissions and machine operations reflect real-world conditions.

## Slide 5
02
System Overview

## Slide 6
Purpose
Enable secure, automated, and intelligent control of a molding station with live data sharing to a 3D model.

## Slide 7
Key Features:
1
Environmental Monitoring: temperature, humidity, air quality, light
Machine Health Monitoring: RPM, vibration, voltage, current, power
4
2
Secure Access Control: RFID authorization
AGV (Automated Guided Vehicle) tracking using obstacle detector node
5
Energy Management: fan/heater status
3
3D Digital Twin: real-time visualization and decision feedback
6

## Slide 8
Communication
All nodes transmit sensor data to a central Cloud platform called ThingsBoard enabling bi-directional control.

## Slide 9
03
Node Architecture

## Slide 10
Node | Function | Controller | Key Sensors | Key Actuators
1. Access Control System | Manages secure entry using RFID | ESP32 Dev Board | RC522 RFID Reader | Servo motor, Buzzer, Red/Green LEDs
2. Environmental Monitoring | Tracks temperature, humidity, air quality, and light | ESP32 Dev Board | DHT11, MQ135, LDR | LED, Buzzer
3. Energy Management | Monitors device status (heater, fan, light) | ESP32 Dev Board | INA219, Push Button | Incandescent Bulb, Heater, DC Motor (fan), 16×2 LCD, Relay
4. Motor Monitoring | Monitors RPM, temperature, V/I, motor diagnostics | ESP32 Dev Board | INA219, MLX90614, Photoelectric Speed Sensor | DC Motor, Servo Motor, Solid State Relay, 1.3″ OLED, Green LED
5. Lathe Monitoring | Tracks vibration, and power | ESP32 Dev Board | INA219, VL6180X, Piezoelectric Sensor | LR7843 MOSFET, DC Motor, 1.3″ OLED, LED, Buzzer, SG90 Servo
6. Motion Detector | Detects movement near the entry door | ESP32 Dev Board | PIR Motion Sensor | Servo Motor, Green LED
7. Obstacle Detector | Detects AGV movement or obstruction | ESP32 Dev Board | Ultrasonic Sensor HC-SR04 | Buzzer, Red LED
8. Temperature Control | Measure the room temperature | ESP32 Dev Board | LM35 | 5V DC Fan, Relay, Red LED
Node Architecture

## Slide 11
04
Functional Workflow

## Slide 12
Entry Authorization
The Access Control System authenticates the user via RFID. The Motion Detector confirms physical presence. The Obstacle Detector checks for AGV movement near the door.

## Slide 13
Access Logic
Entry is permitted only if:
1
RFID credentials are valid
2
No AGV/robotic arm is in the doorway
3
All environmental and machine parameters are within safe limits
If any condition fails, the servo-controlled door remains locked.

## Slide 14
Real-Time Monitoring & Control
Environmental, energy, and machine data stream to the Cloud platform. Nodes respond automatically; for example, if temperature rises, it indicates that the machinery is working inside.

## Slide 15
3D Digital Twin
A web-based 3D model mirrors the physical station.
Bidirectional Feedback:
Live sensor data animates the robotic arm, AGV, and door in the 3D model. Commands from the 3D interface can trigger actuators in the real system.

## Slide 16
05
Key Features

## Slide 17
Key Features
Safety and Security: Access is conditional on machine status and AGV movement.
1
Predictive Maintenance: Motor and lathe monitoring detect faults before failure.
3
Energy Efficiency: Real-time energy tracking optimizes power consumption.
Scalability: Modular node design allows easy addition of sensors or new stations.
2
4

## Slide 18
06
Hardware & Software

## Slide 19
Hardware
ESP32 (multiple variants): ESP8266, ESP32-C6, ESP32-S3, ESP32-WROOM, sensors/actuators as listed above.
Software
Arduino IDE, MQTT, ThingsBoard, Three.js for 3D visualization.
Protocols
Wi-Fi, MQTT, HTTP, Socket.io.

## Slide 20
07
Applications

## Slide 21
Applications
1
Smart manufacturing & Industry
3
Energy-aware production floors
2
Secure industrial zones
4
Digital twin–based predictive analytics

## Slide 22
08
Future Enhancements

## Slide 23
Future Enhancements
AI-driven fault prediction
1
Edge computing for faster local decision-making
2
Integration with robotic arms and automated conveyor systems
3

## Slide 24
Thank You